## Slide 1
🧫
Automated Bacterial Colony Counter
Classical Computer Vision + Random Forest Countability Classifier
AVIT Faculty Hackathon 2026 · Project 07
CSE × Biotechnology · AVIT, VMRF Deemed University, Chennai
Dr. S. Pitchumani Angayarkanni | Mr. R. Udaya | Dr. Baskar | Dr. A. Keerthi
Domain Expert: Dr. S. Kalaivani Priyadarshini, Associate Professor, Department of Biotechnology, Lady Doak College, Madurai
Notes: Welcome. This is Project 07 of the AVIT Faculty Hackathon 2026. We built an automated bacterial colony counter using classical computer vision — no deep learning for counting — plus a Random Forest to assess plate countability. 10-minute talk; 3-minute demo follows.

## Slide 2
PROBLEM STATEMENT
Why Automate Colony Counting?
⏱
Time-Consuming
30–60 min per plate set manually
👁
Subjective
Inter-operator variability up to 15%
❌
Error-Prone
Touching colonies cause miscounts
🔁
Not Reproducible
Lighting & fatigue affect results
Our Solution
✓ Deterministic CV counting — no training data needed
✓ Marker-Controlled Watershed separates touching colonies
✓ 4 methods compared per image
✓ Random Forest for plate-level assessment (TFTC / Countable / TNTC)
✓ Validated on 104 real E. coli lab images
✓ Interactive Streamlit web application
Notes: Manual colony counting is routine in microbiology but slow, subjective, and hard to reproduce. Our system replaces the counting step entirely with classical image processing — keeping the human in the loop only for edge cases via the RF classifier.

## Slide 3
SYSTEM ARCHITECTURE
7-Stage Classical CV Pipeline
1
Petri Plate
Detection
2
Agar Mask &
Reflection Removal
3
CLAHE
Enhancement
4
Adaptive /
Otsu Threshold
5
Watershed
Segmentation
6
Colony
Filtering
7
Count &
RF Assessment
🔢 Automatic Colony Count
+ CFU/mL Estimate
🤖 RF Plate Assessment
Countable / TFTC / TNTC
Colony filters applied: Area · Circularity · Solidity · Extent · Aspect Ratio · Duplicate Suppression
RF Features (8): Coverage Ratio · Component Count · Mean/Std/Max Area · Brightness Mean/Std · Edge Density
Notes: The pipeline runs in 7 deterministic stages. No training data is needed for counting. The RF only sees 8 image-level statistics and makes a plate-level verdict — it never touches the counting logic.

## Slide 4
COUNTING METHODS
Four Independent Counting Algorithms
Baseline
🔵 Connected Components
Standard blob labelling on binary mask. No watershed. Tends to merge touching colonies.
⭐ Improved
🌊 Marker-Controlled Watershed
Distance transform + local maxima markers guide watershed to separate touching colonies.
Blob Detector
🔬 Laplacian of Gaussian
Scale-space blob detection. Independent reference; over-detects at high density (MAPE 143%).
🏆 Final Output
🎯 Consensus Counter
Weighted combination of all methods. Best overall accuracy (MAE 42.12, R² 0.422).
Notes: Each image is processed by all four methods simultaneously. The Consensus combines their outputs. This comparison lets us benchmark the improved Watershed against the standard Connected Components baseline on every single plate.

## Slide 5
QUANTITATIVE RESULTS
Baseline vs. Improved: Method Comparison
Method
MAE ↓
MAPE (%) ↓
R² ↑
Rank
Connected Components (Baseline)
48.32
32.93
0.185
4th
Marker-Controlled Watershed
42.18
35.22
0.421
2nd
Laplacian of Gaussian
73.09
142.91
-0.187
3rd
Consensus Counter ★
42.12
35.19
0.422
1st
Key Insights
▸ Watershed improves R² by 2.3× over Connected Components (0.421 vs 0.185)
▸ LoG over-detects at high density — MAPE 143% excludes it from primary ranking
▸ Consensus edges Watershed for best overall MAE (42.12) and R² (0.422)
* Metrics calculated on countable plates only (manual count 25–250 CFU); TFTC/TNTC excluded.
Notes: The Watershed method gives the most significant improvement. The LoG is useful as a reference but should not dominate the consensus for dense plates. All metrics are computed only on countable plates — this is methodologically important.

## Slide 6
ML CLASSIFIER
Random Forest Plate Assessment
80.8%
Overall Accuracy
0.667
Precision (Countable)
0.889
Recall (Countable)
0.762
F1 Score (Countable)
Class
Precision
Recall
F1
Support
Countable
0.67
0.89
0.76
9
Not Countable (TNTC/TFTC)
0.93
0.76
0.84
17
Overall (Weighted)
0.84
0.81
0.81
26
High recall (0.89) ensures valid plates are rarely missed. High not-countable precision (0.93) prevents TNTC/TFTC plates from being wrongly auto-counted.
Notes: The RF uses 8 extracted image statistics. 80.8% accuracy on 26 held-out plates. The high recall for countable plates is the critical metric — we don't want to miss a valid plate. The class imbalance mirrors real lab conditions where dense plates dominate.

## Slide 7
ROBUSTNESS ANALYSIS
Performance Under Imaging Perturbations
🌑
Low Illumination
Gamma-darkened image
< 10 count deviation
on most plates
✅ Robust
☀️
High Illumination
Gamma-brightened image
< 8 count deviation
on most plates
✅ Robust
📡
Gaussian Noise
σ-noise injected
Dense plates collapse
to 0 detections
⚠️ Fragile
Sample Deviation Data
Plate
Normal
Dark Δ
Bright Δ
Noisy Δ
T4 10⁻⁷ (manual: 59)
67
+3
+5
−67 ✗
T2 10⁻⁵ (manual: 150)
123
−2
−4
−122 ✗
T1 10⁻⁸ (manual: 19)
28
−4
+2
−28 ✗
Notes: The system handles realistic lighting variations well. The critical gap is Gaussian noise — high-frequency noise destroys the binary mask. A denoising pre-processing step (bilateral filter or NLM) is the top priority for the next version.

## Slide 8
LIVE DEMO
Streamlit Application — Demo Walkthrough
01
Upload Plate Image
Single JPG or ZIP of 100+ images — browser or large-ZIP path
02
Select CV Method
Consensus (recommended) or individual method for comparison
03
Tune Parameters
Adjust thresholding, area range, circularity, marker distance
04
Preview Single Plate
See original → mask → binary → overlay with count
05
Process All & Validate
Compare automatic vs manual counts; MAE / MAPE / R² dashboard
06
Download Report
CSV agreement table + classification report + robustness table
GitHub: Pitchumca/colony-counter_IntelliSphere · Deployed on Streamlit Community Cloud
Notes: 3-minute live demo. Navigate to the Streamlit app. Upload the sample ZIP. Show the single-plate preview panel — point out original, mask, overlay. Click Process All and show the results dashboard. Export the CSV. Keep it fast.

## Slide 9
LIMITATIONS & FUTURE WORK
What We Learned & Where We Go Next
⚠ Current Limitations
• Gaussian noise collapses dense plate detection
• High-density countable plates (150–250 CFU): MAPE 43–47%
• RF evaluation limited to 26-plate split
• Validated on E. coli / LB agar only
• LoG inflates consensus error at high density
🚀 Future Directions
✦ Add bilateral / NLM denoising pre-processing
✦ Density-conditional LoG weight in Consensus
✦ Optional deep learning (SAM / Mask R-CNN) for very dense plates
✦ Expand to multi-species, multi-agar validation sets
✦ Tablet app with auto-capture & real-time CFU display
Notes: Be honest about limitations — the noise fragility is a clear gap. The good news is the fix is straightforward: a denoising step before thresholding. Future work is concrete and already scoped.

## Slide 10
CONCLUSIONS
Key Takeaways
🎯
80.8% Plate Classification
RF correctly assesses countable vs TNTC/TFTC with high recall (0.89)
🌊
2.3× R² Improvement
Watershed over Connected Components baseline (0.421 vs 0.185)
📊
42.12 MAE / 0.422 R²
Consensus counter is best overall; 64.81% counting accuracy
🛡
Robust to Light Changes
< 10 count deviation under dark/bright perturbations
Classical CV + lightweight ML delivers a practical, explainable, deployment-ready colony counter for real laboratory use.
Notes: Close by reinforcing that this system is already deployed on Streamlit, validated on 104 real images, and the source is on GitHub. Classical CV + RF keeps the pipeline explainable — important for laboratory adoption. Thank the audience and open for questions.